## Slide 1
Trying to outsmart a compiler defeats much of the purpose of using one.
Brian Kernighan

## Slide 2: Principles of Compiled Code
NI(E)-GEN, Spring 2023
https://courses.fit.cvut.cz/NI-GEN
Notes: Details about how compiled code actually works. Information about calling conventions, stack frames, variables, symbols and visibility. Memory areas (heap, stack, globals), alignment. Compilation units (modules, functions, basic blocks). Object files, static vs dynamic linkage, etc.

## Slide 3: So we have a compiler…

## Slide 4
Notes: So we know how to compile and what are all the aspects in the overview.

## Slide 5
???
???
???
???
???
Notes: So we know how to compile and what are all the aspects in the overview.

## Slide 6: Executables

## Slide 7: Executable
contains binary data of various kinds partitioned in sections (.text, .data, .rodata, etc.)

## Slide 8
.text:
mov eax, hello_world
…
.rodata
hello_world:
“hello all, this is a text”, 0
.data
global-var:
0x67

## Slide 9: Executable
contains binary data of various kinds partitioned in sections (.text, .data, .rodata, etc.)
when executed, the section contents are copied to memory

## Slide 10
System
.text
.rodata
.data

## Slide 11
System
.text
.rodata
.data

## Slide 12
System
.text
.rodata
.data
.text’
.rodata’
.data’

## Slide 13: Relocation
absolute addresses of symbols cannot be known statically
executable contains a relocation table
  address to be patched
  target symbol
  patch type
the loader then updates the section contents based on the relocation table once the section starts are known

## Slide 14: Executable
contains binary data of various kinds partitioned in sections (.text, .data, .rodata, etc.)
when executed, the section contents are copied to memory
and relocated

## Slide 15
.text
.rodata
.data
.text’
.rodata’
.data’
System

## Slide 16: Executable
contains binary data of various kinds partitioned in sections (.text, .data, .rodata, etc.)
when executed, the section contents are copied to memory
and relocated (if necessary, such as libraries)

## Slide 17
.text
.rodata
.data
.text’
.rodata’
.data’
System

## Slide 18
.text
.rodata
.data
.text’
.rodata’
.data’
System

## Slide 19: Executable
contains binary data of various kinds partitioned in sections (.text, .data, .rodata, etc.)
when executed, the section contents are copied to memory
and relocated (if necessary, such as libraries, or ASLR)
Notes: Address Space Layout Randomization

## Slide 20
OK
???
???
???
OK
Notes: So we know how to compile and what are all the aspects in the overview.

## Slide 21: Object Files

## Slide 22: Object Files
like executable
+ more sections, - loader
a lot more relocations
more information so that link-time optimization can be performed

## Slide 23
OK
OK
???
???
OK
Notes: So we know how to compile and what are all the aspects in the overview.

## Slide 24: Source Granularity

## Slide 25: Source Granularity
project
executable & libraries
files
functions
basic blocks
statements

## Slide 26: Basic Block
code sequence with single entry and single leave point (terminating instruction)
once first instruction in a basic block gets executed, all instructions in basic block will execute sequentially
no control flow

## Slide 27
if (a < 0) {
a = a + 1;
} else {
b = b + 1;
}
c = a + b;

## Slide 28
if (a < 0) {
a = a + 1;
} else {
b = b + 1;
}
c = a + b;
B0: cmp ax, 0 // a in ax
jge B2
B1: add ax, 1
jmp B3
B2: add bx, 1 // b in bx
B3: mov cx, ax // c in cx
add cx, bx

## Slide 29
if (a < 0) {
a = a + 1;
} else {
b = b + 1;
}
c = a + b;
B0: cmp ax, 0 // a in ax
jge B2
B1: add ax, 1
jmp B3
B2: add bx, 1 // b in bx
jmp B3
B3: mov cx, ax // c in cx
add cx, bx

## Slide 30: Code Generation
BI-PPA, BI-PJP

## Slide 31: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));

## Slide 32: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
f_min: # functions are labels

## Slide 33: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
f_min:
cmp ax, bx # arguments in
jl x_less # ax and bx regs
x_less:

## Slide 34: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
f_min:
cmp ax, bx
jl x_less
mov ax, bx # result
ret # passed in ax reg
x_less:

## Slide 35: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
f_min:
cmp ax, bx
jl x_less
mov ax, bx
ret
x_less:
ret # already in ax

## Slide 36: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
jmp start # start with start
f_min:
cmp ax, bx
jl x_less
mov ax, bx
ret
x_less:
ret
start: # start exec here
mov ax, 67 # vars in regs

## Slide 37: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
jmp start
f_min:
cmp ax, bx
jl x_less
mov ax, bx
ret
x_less:
ret
start:
mov ax, 67
mov bx, 89

## Slide 38: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
jmp start
f_min:
cmp ax, bx
jl x_less
mov ax, bx
ret
x_less:
ret
start:
mov ax, 67
mov bx, 89
call f_min # luck:) -> ax

## Slide 39: Code Generation
int min(int x, int y) {
return x < y ? x : y;
}
int a = 67;
int b = 89;
print(min(a, b));
jmp start
f_min:
cmp ax, bx
jl x_less
mov ax, bx
ret
x_less:
ret
start:
mov ax, 67
mov bx, 89
call f_min
call print # ax -> ax

## Slide 40: Code Generation
jmp start
f_min:
cmp ax, bx
jl x_less
mov ax, bx
ret
x_less:
ret
start:
mov ax, 67
mov bx, 89
call f_min
call print

## Slide 41: Code Generation
00: jmp start
f_min:
04: cmp ax, bx
08: jl x_less
0a: mov ax, bx
0c: ret
x_less:
0d: ret
start:
0e: mov ax, 67
12: mov bx, 89
16: call f_min
1a: call print

## Slide 42: Code Generation
00: jmp 0e
04: cmp ax, bx
08: jl 0d
0a: mov ax, bx
0c: ret
0d: ret
0e: mov ax, 67
12: mov bx, 89
16: call 04
1a: call print
Linker, help!

## Slide 43: Memory Layout

## Slide 44
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC

## Slide 45
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
main()

## Slide 46
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
1 argument
3 local variables
recursive
return value

## Slide 47: Call Stack
Last In – First Out Structure
Holds local variables, arguments and return addresses
Each function’s data live in its own area called stack frame
When function exits, the frame is popped off the stack

## Slide 48
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
SP
BP
Stack:

## Slide 49
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
SP
BP
start of main()
local vars of main
Stack:
main

## Slide 50
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
Stack:
main
SP
BP

## Slide 51
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
Stack:
main
SP
BP
[BP – 1]

## Slide 52
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 53
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP
[BP + 2]
[BP + 3]
[BP + 4]

## Slide 54
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 55
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 56
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 57
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
Stack:
main
SP
BP

## Slide 58
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
Stack:
main
SP
BP

## Slide 59
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 60
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 61
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 62
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 63
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 64
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP
1

## Slide 65
fib(1)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP
1

## Slide 66
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
1
old BP
ret address
tmp
tmp2
tmp3
Stack:
main
SP
BP
1

## Slide 67
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP
1

## Slide 68
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
Stack:
main
SP
BP
1

## Slide 69
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
Stack:
main
SP
BP

## Slide 70
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
Stack:
main
SP
BP

## Slide 71
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
Stack:
main
SP
BP

## Slide 72
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 73
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 74
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP

## Slide 75
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
tmp
tmp2
tmp3
Stack:
main
SP
BP
Stack Overflow

## Slide 76
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
0
tmp2
tmp3
Stack:
main
SP
BP

## Slide 77
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
0
tmp2
tmp3
Stack:
main
SP
BP

## Slide 78
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
0
1
tmp3
Stack:
main
SP
BP

## Slide 79
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
0
1
tmp3
Stack:
main
SP
BP

## Slide 80
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
0
1
1
Stack:
main
SP
BP

## Slide 81
fib(2)
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
0
1
1
Stack:
main
SP
BP
1

## Slide 82
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
tmp2
tmp3
2
old BP
ret address (PC)
0
1
1
Stack:
main
SP
1
BP

## Slide 83
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
1
tmp3
Stack:
main
SP
1
BP

## Slide 84
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
1
tmp3
Stack:
main
SP
BP

## Slide 85
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
1
2
Stack:
main
SP
BP

## Slide 86
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
1
2
Stack:
main
SP
BP

## Slide 87
fib(3)
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
1
2
Stack:
main
SP
BP
2

## Slide 88
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
3
old BP
ret address (PC)
1
1
2
Stack:
main
SP
BP
2

## Slide 89
int fib(int n) {
if (n == 0)
return 0
if (n == 1)
return 1
int tmp = fib(n – 2)
int tmp2 = fib(n – 1)
int tmp3 = tmp1 + tmp2
return tmp3
}
fib(3)
AX
BX
CX
DX
PC
start of main()
local vars of main
Stack:
main
SP
BP
2

## Slide 90: Call Stack
stack frames used also for nested blocks
elements on stack must have statically known sizes
slightly more complicated for languages that allow nested functions
  stack frame saves the old BP as well as BP to the closest parent function
when function returns data on stack cease to exist
  this is not ok for other than local variables
why?

## Slide 91: Data Segment
stores global variables
has statically known size
data in DS are valid throughout the duration of the program
Is this always true?
Notes: Not always true, they may need to be initialized first

## Slide 92: Data Segment
stores global variables
has statically known size
data in DS are valid throughout the duration of the program
But so does stack!!
Where to put dynamically sized data?

## Slide 93: Heap
memory area for dynamically allocated data
allows allocation & deallocation in arbitrary order
manual or automatic (garbage collector) management
dynamic size depending on the actual allocation at any given time (sort of)

## Slide 94: Memory Layout
0
max mem
Code Segment
Data Segment
Heap
Stack

## Slide 95: Calling Conventions

## Slide 96: Calling Conventions
how to pass arguments?
  stack, registers, both, argument order
how to return the result of the function?
  stack, registers, type-dependent
which registers are free for caller, and which for callee
who is responsible for cleanup?
  caller cleanup, callee cleanup
architecture, OS, and language dependent

## Slide 97: cdecl (x86)
Microsoft’s C compiler, caller saved
arguments on stack, right to left
result in eax, st0, or stack
eax, ecx, edx caller saved, rest callee saved

## Slide 98: cdecl (x86)
push ebp ; save caller’s frame and start new frame
mov ebp, esp
push 3 ; push the arguments left to right
push 2
push 1
call f ; call function f
add esp, 12 ; remove arguments from frame (caller saved)
add eax, 1 ; result returned in eax (if integer)
mov esp, ebp ; ebp is callee cleaned (call to itself!)
pop ebp
ret

## Slide 99: cdecl (x86)
sometimes the bp is updated by callee (BP - addressing in callee, like our example)
larger results returned on stack (caller allocated)
results in more registers (eax:edx typically)
stack alignment considerations

## Slide 100: Other x86 Calling Conventions
fastcall (arguments in registers, callee cleanup)
thiscall (this pushed on stack as first argument, some variants in ecx, caller cleanup)
stdcall (callee cleanup, right to left args, Win32API)
x86_64 calling conventions (Microsoft vs the world)

## Slide 101: ARM (A32)
link register (LR) for return address
  faster than stack for calls to leaf subroutines
  not really that necessary with inlining
more registers
  r0, r1, r2, r3 = arguments (callee saved)
  r4 – r11 = local variables (callee saved)

## Slide 102: ARM64
even more registers
r19-r29 callee saved
r9 – r15 caller saved
r0-r7 arguments and results

## Slide 103: Target Architectures

## Slide 104: Target Architectures
x86, x86-64, ARM, RISC-V, MIPS, Itanium, Sparc, AVR, …, …
RISC, CISC, EPIC
all have memory, registers, instructions
Notes: Talk a bit about the target architectures (RISC, CISC, etc.). Registers and all the basic stuff we need to compile to.

## Slide 105: CISC
memory is fast(!), and pricey
clock speed is function of available technology only, cpu size & power is not an issue
since there are transistors to spare, complex CPU instructions are possible and they greatly speed up the program and lower the memory requirements
1960

## Slide 106: CISC
reg-mem arithmetics
very complex addressing modes
special instructions to support calls, control flow and other higher level language features
variable instruction length
1960

## Slide 107: CISC
memory is fast(!), and pricey
clock speed is function of available technology only, cpu size & power is not an issue
since there are transistors to spare, complex CPU instructions are possible and they greatly speed up the program and lower the memory requirements
1980

## Slide 108: CISC
memory is slow and cheap
clock speed is largely function of cpu size & power
cpu features on die compete with caches, pipeline stages, super-scalar ALUs, etc., there are no transistors to spare, complex instructions make the whole CPU slower
1980

## Slide 109: RISC
reg-reg arithmetics
simple addressing modes
fixed instruction length
highly regular decoding
1980

## Slide 110: SuperScalar Processors
as instruction is processed by the CPU, different parts are utilized
instead of idling the unused circuits, more instructions can be processed at the same time
instruction pipeline
Notes: Talk about pipeline saturation and draw an image

## Slide 111: Pipeline Stalls
pipeline only helps if it is full
branches, more complex ALU operations, data dependencies, memory accesses may cause holes (stalls) in the pipeline
the instructions must be scheduled to minimize these
Notes: Talk about branch delay slot

## Slide 112: RISC
small, fast to execute instructions soon reached the limit of 1 IPC
clock rates limited by technology & power
can we go below 1 IPC?
1980

## Slide 113: VLIW
Very Large Instruction Words
large instructions encoding multiple smaller operations
that are executed in parallel
(the compiler schedules the operations into the VLIWs ahead of time)

## Slide 114: EPIC
non-determinism of memory access is a problem for VLIW
Mitigated by EPIC (Explicitly Parallel Instruction Computing) where instructions and continuation logic is put by compiler into bundles
explicit prefetching, explicit speculative pre-loading, predicated execution all used to make the bundles into more deterministic sequence
Intel Itanium
Notes: Talk a bit about itanium and how x86_64 eventually got the upper hand

## Slide 115: The Awesome Compiler

## Slide 116: The Awesome Compiler
Not so much…

## Slide 117: Super-Super Processors
as superscalar or EPIC processors got more and more complex and powerful, the scheduling demands placed on the compiler were too great
multiple execution units per stage were added to lower the congestion
the super-super architecture

## Slide 118: SMT
often computers do more than one thing anyways
SMT (Simultaneous Multithreading) makes multiple “cores” share parts of the execution units
better utilization of the resources
no thread context switching required
Hyperthreading

## Slide 119: Out of Order Execution
CPU keeps a pool of fetched instructions
these are issued dynamically not according to their order in program, but availability of required execution units and inputs
requires complex bookkeeping to preserve sequential semantics
makes compiler scheduling much less important

## Slide 120
https://en.wikipedia.org/wiki/Nehalem_(microarchitecture)#/media/File:Intel_Nehalem_arch.svg

## Slide 121: Practical ISA

## Slide 122
struct pos {
int32_t x;
int32_t y;
};
pos items[128];
int32_t j = items[i].y;
// r1 contains & items
// r2 contains i
ldi r3, r2
shr r3, 3
add r3, r1
ldi r4, 4
add r3, r4
load r4, r3
* by 8 (sizeof pos)
load from memory

## Slide 123
struct pos {
int32_t x;
int32_t y;
};
pos items[128];
int32_t j = items[i].y;
// edx contains & items
// eax contains i
mov eax, [edx + 8 * eax + 4]
j
i
items
sizeof pos
y’s offset

## Slide 124
struct pos {
int32_t x;
int32_t y;
};
pos items[128];
int32_t * j = & items[i].y;
// r1 contains & items
// r2 contains i
ldi r3, r2
shr r3, 3
add r3, r1
ldi r4, 4
add r3, r4
r3 contains the address

## Slide 125
struct pos {
int32_t x;
int32_t y;
};
pos items[128];
int32_t * j = & items[i].y;
lea eax, [edx + 8 * eax + 4]

## Slide 126: Fun with CISC
complex instructions not created equal
some are deprecated (made slower), or made faster
often complex instructions can be used for surprising purposes
consider lea
Notes: Talk about weirdly designed instruction sets
LEA used for add as it is more powerful & faster often

## Slide 127
lea ecx, [edx + 8 * eax + 4]

## Slide 128
lea ecx, [edx + 8 * eax + 4]
mov ecx, eax
shl ecx, 3
add ecx, 4
add ecx, edx

## Slide 129: Code Size Matters
variable length encodings even on RISC ISAs
immediate argument sizes
relative branch distances
not all registers created equal

## Slide 130: General Trends
out-of-order execution and more regular pipelines
RISC architecture is becoming increasingly complex
Notes: Maybe just talk about this

## Slide 131: Further Reading
https://medium.com/swlh/what-does-risc-and-cisc-mean-in-2020-7b4d42c9a9de